## Slide 1: Cost Optimization Models for SRF Linacs
Tom Powers
TTC Workshop June 2013 Final

## Slide 2: Overall Cost Calculation
Calculate Loaded-Q’s
Including
Variance
How Many
Cryomodules?
Permutations on RF Power
Calculate
Linac Hardware Costs
Determine Qo
At E and F
Calculate Heat
Load w/Margin
Number of Plants?
Calculate AC Efficiency
Calculate Cryo Plant Costs
Calculate Linac Civil Costs
Calculate AC Power Overhead
And 10 Year Costs
Include Inner Cryomdule Girders
And Controls
Determine Linac AC PWR
Calculate Cost
Calculate Cryo
Infrastructure Costs

## Slide 3: Cryogenic Plant Considerations
A 2 K liquid helium cold box is limited by transportation infrastructure to about 18 kW at 4 K which equates to 5 kW at 2 K, and 3.8 kW at 1.8 K.*
It is beneficial from a design and maintenance standpoint to build mulitple copies of the same plant.
For these reasons in the model, any time that the plant exceeds a multiple of 5kW @ 2K the plant was split into two identical plants and the efficiency will come from the following curve.
The cost of a cryo plant doubles (at least) if you buy it turn key rather than buying the components, (compressors, coldboxes, oil removal systems, etc.) seperately.*
For this model we used $25M for the cost of a 5 kW@2K plant and $5M for civil and infrastructure costs (based on the CEBAF 12 GeV project).
The costs were escalated and the efficiency reduced by 30% at 1.8K. These factors can be adjusted by the user.
*Dana Arenius, Jefferson Lab, Personal Communication

## Slide 4: Cryo Plant Efficiency as a Function of Heat Load
Ganni, R., et. al., “Cryogenic Systems Improvements,” JLAB Science and Technology Review, May, 2008.

## Slide 5: Resultant Cost and Efficiency Curves for the Cryo Plant

## Slide 6: Different Approaches for Optimization.
Non causal cryomodules. Smooth curves of frequency dependence by.
  Using a fixed active length per cryomodule and thus a fixed number of cryomodules,
  Using fractional number of cavities within each cryomodule.
Variable number of cells per cavity and cavities per cryomodule.
  Scale shunt impedance as 1/f.
  Provides curves that have steps as you change cavity parameters and number of cryomodules
Variable gradient for specific cavity/cryomodule designs
  Effectively optimizes on the number of cryomodules to reach the design energy gain.
  Provides smooth results with steps for cryo plant configurations.

## Slide 7: Qo Calculations
Q0 as a function of frequency and temperature at 16 MV/m. All frequencies scaled from CEBAF C100 upgrade cavity.
Q0 is calculated for each data point, and is based on a compilation of historic data. This historical data is a compilation from measurements taken in the vertical test area at Jefferson Lab.*
*Ciovati, G., et. al., “Residual Resistance Data from Cavity Production Projects at Jefferson Lab,” IEEE Transactions on Applied Superconductivity, Vol 21, No. 3, June 2011

## Slide 8: SRF Parameters Variables
Includes
General cavity parameters
Beam current and phase
Detune allowance for microphonics, helium pressure variations, tuning uncertainty, etc.
RF power margin
Maximum allowed loaded-Q
Material type and treatment
Linac energy
Linac Packing factor (Total L / Active L)
ERL? Uses resultant current and tune up beam for RF Power calculations

## Slide 9: Baseline Costs Variables
Cryomodule fixed cost includes installation and testing.
RF power costs includes transmission, circulators, etc.
Inner cryomodule girder includes magnets, controls, valves, viewers, etc.
Tunnel civil costs includes service buildings, AC power, LCW, etc.
Cryo plant is based on CEBAF upgrade costs assumes you buy the major components double or triple the cost if you buy a turn-key plant.
Linac R&D costs includes prototype cryomodule as well as remainder of electronics.

## Slide 10: Other Inputs/Controls
Ability to what if Qo improvements by adjusting scale and slope.
ERL parameters to adjust resultant current and tune beam.
Temperature array allows one to change the parameter.
Cryomodule type allows one to select between several types with one being user defined. This is only used on the sweep gradient module.
Beam current slider.
Also have buttons to pause, save results, save and restore set up parameters.

## Slide 11: Output Parameters
Costs of different components of the overall costs.
10 year AC power costs
Linac Length
Match Loaded Q
Qo at E and F
RF power per cavity
All output parameters during a sweep can be written to a file or viewed on live graphs.

## Slide 12: Summary
Executable files (Windows 32 Bit and Windows 64 bit) will be available by the end of next week at:
https://userweb.jlab.org/~powers/
Demonstration to follow
Comments and suggestions welcome.

## Slide 13: Backup Slides

## Slide 14: Jlab Cryomodule Cost History
Data taken from closed projects, C100 is estimated
Engineering costs included
Overhead Rates lowered for C100,SNS,CEBAF projects
XFEL estimate ~$1.7M?
ILC estimate ~$1M?
A. McEwen

## Slide 15: QL Optimization for Minimum Power
Depending on the application (injector/LINAC or ERL) the cavity QL must be optimized for minimum power.
Beam Loaded Cavity
Lightly-non beam loaded Cavity
Chart: 
| 4000000 | 5000000 | 6000000 | 7000000 | 8000000 | 9000000 | 10000000 | 13000000 | 16700000 | 20000000 | 25000000 | 30000000 | 40000000 | 50000000 | 60000000 | 70000000 | 80000000 | 90000000 | 100000000 | 200000000 | 300000000 | 400000000
0 Hz | 27282.0644 | 23526.941 | 21076.7271 | 19372.1758 | 18133.6637 | 17205.8443 | 16495.5099 | 15167.5278 | 14423.7055 | 14176.8337 | 14191.9142 | 14467.9766 | 15411.5743 | 16616.154 | 17951.2246 | 19360.8614 | 20817.1022 | 22304.4122 | 23813.4707 | 39382.5229 | 55212.5569 | 71107.8364
5 Hz | 27295.7065 | 23543.9935 | 21097.1902 | 19396.0494 | 18160.9478 | 17236.5389 | 16529.615 | 15211.8644 | 14480.661 | 14245.0439 | 14277.177 | 14570.292 | 15547.9948 | 16786.6796 | 18155.8553 | 19599.5972 | 21089.9431 | 22611.3583 | 24154.5219 | 40064.6252 | 56235.7104 | 72472.0411
10 Hz | 27338.2987 | 23597.2338 | 21161.0785 | 19470.5859 | 18246.1323 | 17332.3715 | 16636.0956 | 15350.2892 | 14658.4837 | 14458.0052 | 14543.3785 | 14889.7338 | 15973.9173 | 17319.0827 | 18794.739 | 20344.9616 | 21941.7881 | 23569.6838 | 25219.3281 | 42194.2376 | 59430.129 | 76731.2659
20 Hz | 27503.6568 | 23803.9315 | 21409.1158 | 19759.9626 | 18576.8486 | 17704.4273 | 17049.4909 | 15887.7032 | 15348.8539 | 15284.7959 | 15576.8669 | 16129.9199 | 17627.4987 | 19386.0594 | 21275.1111 | 23238.729 | 25248.9509 | 27290.242 | 29353.2816 | 50462.1446 | 71831.9895 | 93267.0798
Cavity Detuning
Chart: 
| 4000000 | 5000000 | 6000000 | 7000000 | 8000000 | 9000000 | 10000000 | 13000000 | 16700000 | 20000000 | 25000000 | 30000000 | 40000000 | 50000000 | 60000000 | 70000000 | 80000000 | 90000000 | 100000000 | 200000000 | 300000000 | 400000000
0 Hz | 19644.4073 | 15729.6945 | 13119.8914 | 11255.7508 | 9857.6494 | 8770.2407 | 7900.317 | 6093.567 | 4759.2644 | 3985.7479 | 3202.882 | 2680.9979 | 2028.7028 | 1637.3895 | 1376.5672 | 1190.3111 | 1050.659 | 942.0762 | 855.2418 | 465.365 | 336.4701 | 272.8206
5 Hz | 19658.0493 | 15746.7471 | 13140.3544 | 11279.6244 | 9884.9335 | 8800.9353 | 7934.4221 | 6137.9036 | 4816.2199 | 4053.9581 | 3288.1447 | 2783.3133 | 2165.1232 | 1807.9151 | 1581.1979 | 1429.047 | 1323.4999 | 1249.0222 | 1196.293 | 1147.4673 | 1359.6236 | 1637.0253
10 Hz | 19700.6415 | 15799.9874 | 13204.2428 | 11354.1608 | 9970.118 | 8896.7679 | 8040.9027 | 6276.3285 | 4994.0425 | 4266.9194 | 3554.3463 | 3102.7551 | 2591.0457 | 2340.3182 | 2220.0816 | 2174.4113 | 2175.3449 | 2207.3478 | 2261.0992 | 3277.0797 | 4554.0422 | 5896.2501
20 Hz | 19865.9997 | 16006.6851 | 13452.28 | 11643.5376 | 10300.8343 | 9268.8237 | 8454.2981 | 6813.7424 | 5684.4128 | 5093.7101 | 4587.8347 | 4342.9412 | 4244.6271 | 4407.2949 | 4700.4537 | 5068.1787 | 5482.5077 | 5927.9059 | 6395.0526 | 11544.9867 | 16955.9026 | 22432.0641
I = 10 mA
I = 1 mA
Notes: Beam loading pushes the QL lower …..less susceptible to microphonics.
Lightly loaded cavities, like and ERL, may have QLs closer to 5e7

## Slide 16: Allow for Transient Beam Loading?
0
No Transient Loading
1 Measured gradient
2 Measured phase
3 Magnitude drive
4 Phase drive
Tune Beam Transient, 600 uA, Phase  0°
Measured and predicted RF drive amplitude and phase due to CW beam loading in an ERL where the effective current is approximately 7% of the single pass beam at 75º.